## Slide 1
Course: 19ECE311 – Computer Networks Semester: S6 – BTech ECE
HOTEL NETWORK MANAGEMENT SYSTEM

## Slide 2
GROUP MEMBER
nived s – AM.EN.U4ECE22032
Noaf N– AM.EN.U4ECE22034
vaishnav mohan– AM.EN.U4ECE22050

## Slide 3
The Hotel Network Project is designed to build a secure, reliable computer network across three floors of a hotel.
The system uses VLANs for each department, OSPF for inter-router communication, and DHCP for automated IP configuration.
It aims to improve internal communication, streamline operations, and enhance guest experience through robust IT infrastructure.
INTRODUCTION

## Slide 4
Objectives
  Design a scalable and secure hotel network using hierarchical topology
  Implement VLANs for departmental isolation and efficient management
  Automate IP address distribution using DHCP
  Provide remote management through SSH
  Implement port security and wireless connectivity

## Slide 5
  Proper placement of routers and switches in multi-floor buildings
  Use of VLANs, firewalls, and encryption for data security
  Server room design for efficient distribution
  Regulatory compliance with GDPR and privacy laws
  Detailed documentation and proactive testing of network performance
LITERATURE REVIEW

## Slide 6
  3 routers (each floor) placed in the IT server room
  Floor-wise switches with trunk ports and VLAN tagging
  Wireless Access Points and printers per department
  OSPF routing protocol for inter-router communication
  DHCP for automated IP assignment
  SSH for secure remote management
PROPOSED
DESIGN

## Slide 7
VLAN & IP PLANNING
  Admin (VLAN 20) – 192.168.2.0/24
  IT (VLAN 10) – 192.168.1.0/24
  Finance (VLAN 50) – 192.168.5.0/24
  HR (VLAN 40) – 192.168.4.0/24
  Sales (VLAN 30) – 192.168.3.0/24
  Reception (VLAN 80) – 192.168.8.0/24
  Store (VLAN 70) – 192.168.7.0/24
  Logistics (VLAN 60) – 192.168.6.0/24
1st Floor
2nd Floor
3rd Floor

## Slide 8
IMPLEMENTATION HIGHLIGHTS
  Routers connected using serial DCE cables
  Subinterfaces configured for each VLAN
  DHCP pools set up on each router for dynamic IP assignment
  SSH login set up with usernames and passwords
  Port fa0/1 on IT switch secured for only Test-PC
  Wireless networks configured and mapped to VLANs

## Slide 9
VLAN communication was successfully tested using ping and traceroute, while DHCP accurately assigned IPs across all VLANs. SSH access was configured and confirmed for secure remote router management. Port security effectively blocked unauthorized devices, and wireless connectivity was available on all floors with correct VLAN mapping.
RESULTS

## Slide 10
The project successfully demonstrated the creation of a reliable and scalable hotel network using Cisco Packet Tracer. Key features implemented include OSPF routing, DHCP-based IP management, secure VLAN configuration, wireless and printer integration, and remote access via SSH. For future enhancements, the network can be strengthened by adding firewall rules, integrating cloud-based monitoring and logging, and expanding support for smart hotel devices and IoT-based services.
CONCLUSION

## Slide 11
References
  Forouzan, B. A. – Computer Networks (2012)
  Cisco – Data Communications (2021, 2022)
  Stallings, W. – OSPF Configuration Guide (2013)
  Cisco – VLAN, DHCP, SSH, and Port Security Docs
  Hotel Technology – Wireless LAN Config Guide (2022)

## Slide 12
THANK YOU